## Slide 1: CODES-Tracer tutorial
erhtjhtyhy
Neil McGlohon
PhD Student Researcher
Department of Computer Science
Rensselaer Polytechnic Institute
Adapted from N. Jain and M. Mubarak’s slides for HOTI2017
Enabling hpc design space exploration via discrete-event simulation
Nikhil jain
Compute Architect
NVIDIA

## Slide 2: slides
Available for download at:
  http://nikhil-jain.github.io/codes-hoti.pptx
  https://github.com/codes-org/codes
  https://github.com/ROSS-org/ROSS
  https://github.com/LLNL/TraceR

## Slide 3: Tutorial outline
Session I: Introduction to CODES and TraceR, and their use for simulations
Session II: Replaying HPC workloads, simulating MPI operations and collectives
Session III: Storage simulations, Misc

## Slide 4: PROJECT contributors
Argonne National Laboratory, Mathematics and Computer Science
Lawrence Livermore National Laboratory, Center for Applied Scientific Computing
Nvidia, Compute Arch
Rensselaer Polytechnic Institute, Computer Science
University of Arizona, Computer Science
UC Davis, Computer Science
University of Maryland, Computer Science

## Slide 5
Session I: introduction, case STUDY, and interconnect models

## Slide 6: Goals of session I
Introduction
Case study
Features
HPC Interconnect models
Configuring interconnect simulations
Interpreting simulation output

## Slide 7
Introduction & background

## Slide 8: Building blocks of hpc interconnects
HPC performance is sensitive to the interconnect latency
Interconnects are custom built to achieve maximum throughput
Basic Components:
  Network topology: Arrangement of network nodes and links to maximize performance.
  Routing: The protocol using which a packet selects its next destination. Depends on the underlying network topology.
  Flow control: Allocating network links and buffers to packets as they traverse through the network. Usually independent of the underlying topology and routing protocols.

## Slide 9: Why HPC Interconnect simulation?
HPC interconnects are complex!
Need to look at several factors that influence network performance:
  Interconnect Topology
  Routing
  Quality of Service
  Job placement policies
  Inter-job and intra-job interference
  Storage placement on network
Improved performance is contingent on an optimal combination of the above factors

## Slide 10: Ross: parallel discrete-event simulator
Discrete event simulation (DES): a computer model for a system where changes in the state of the system occur at discrete points in simulation time
Parallel DES allows execution of simulation on a parallel platform
Rensselaer Optimistic Simulator System (ROSS) provides PDES capability for CODES
  Optimistically schedules events. Rollback realized via reverse computation
  Logical processes (LPs) model state of the system
Notes:   ROSS has Logical processes or LPs that model the state of a system for example an LP can be a server in a queueing network.
  Events are issued by these LPs (Logical Processes) and each event computation can modify LP’s state variables and schedule new events in turn. For example, denoting the arrival of a new job at the server.
  ROSS uses time warp synchronization protocol to process events. If the synchronization protocol detects an out of order event, the events are rolled-back and re-executed in the correct order. This enables much richer simulations (e.g., more events) than otherwise possible

## Slide 11: CODES: modeling & Simulation framework
Accelerate HPC system co-design by providing a detailed simulation of HPC interconnects, storage, workloads and surrounding environment
Couple best-of-breed parallel discrete event simulation with experts in interconnects and storage architecture design
Incrementally develop HPC simulation capability, validating approach and components along the way
Complement experimentation on real systems
Figure: CODES Architecture Diagram
Notes: Vision
  Develop an infrastructure that accurately reflects relevant system properties
  Leverage this infrastructure as a tool for investigating HPC architecture design
  Eventually, provide a simulation toolkit to the community to enable broader investigation of the design space

## Slide 12: Tracer: replaying mpi traces
OTF2 traces for MPI
BigSim traces for Charm++, AMPI
Default and user-defined job placement and task mapping
MPI point-to-point semantics and protocols
Inbuilt collectives: tree based bcast, reduce, allreduce, and barrier; message size based algorithms for alltoall and allgather
Simulation time scaling

## Slide 13: Features: HPC Simulations
Packet-level simulations of HPC interconnect topologies
Trace-driven analysis (DUMPI+OTF2), synthetic workloads
Multiple jobs can be replayed on the network
Different job placement schemes can be used
Multiple ranks mapped to network nodes can be used
Detailed statistics generation
MPI collective operations can be simulated
General purpose storage model that uses concurrent, pipelined RDMA read/write requests (simulating burst buffers/SSD)

## Slide 14: simulation stack
Workloads: Session II
System Models in Session I & III
Notes: Workloads
MPI simulation layer + synthetic workloads
MPI simulation layer replays MPI operations from the traces on the CODES HPC system simulations.

## Slide 15
Hpc interconnect models

## Slide 16: Structure of modern interconnect topologies
A 3-ary 3-d Torus network
A 3-level pruned Fat Tree with 64 compute nodes
Torus Network
Homogeneous structure
Dedicated routers per compute node
Fat tree Network
Static Routing
Job placement impacts inter-job interference
Dragonfly Class Networks
Groups with All-To-All Global Connections
Flexible Routing
Strong resilience to inter-job interference
Slim Fly Network
Cost-Effective
Low-Diameter-High-Path-Diversity
Complex Global Link Structure
A 7 Group Dragonfly
An 8 Group Slim Fly
Notes: Torus had a homogenous n-dimensional structure with one router dedicated per compute node. Two nodes used to have a dedicated link between each other. Short electrical links were used.
With high-radix networks such as dragonfly, each router is shared by multiple compute nodes at the first level. The routers in a group are connected to each other in either an all to all structure or a matrix format. Groups are connected to each other via optical links. There is different link connectivity at each of these levels.
Structure of a Cray XC style dragonfly network. Routers within a group are arranged in a two dimensional matrix and there are different types of links at each level.
Routers arranged in a row are connected in an all to all fashion via green electrical links. Chassis.
Across the rows, routers in the same columns are connected to each other via 3 black links.
Across the groups, 12x or 24x optical cables are used. If this optical cable between two groups fails, then one has to reach the group via non-minimal path.
Fat tree networks are also based on high-radix switches. They use static routing though which involves routing tables that need to be rebuild once the network configuration is modified. Job placement is the key to reduce interference in fat tree networks. If the application spans one pod or less than one pod then the routing doesn’t go to top level switches.

## Slide 17: Overview of network models
Multiple network models are supported – 1D/2D Dragonfly, Megafly, Slim Fly, Fat Tree, Express Mesh, Arbitrary graphs, Torus…
Abstraction layer ‘model-net’ sits on top of network models
  Breaks messages into packets
  Offers FIFO, round robin and priority queues
To try different networks, simply switch the network configuration files!
Storage models, MPI simulation and workload replay layers are independent of the underlying networks

## Slide 18: Simple net network model
A latency/bandwidth model where message is directly sent from source to destination
Uses infinite size queuing
Easy setup– uses a startup delay and link bandwidth for configuration
Mostly for debugging/testing purposes-- Can be used as a starting point when replaying MPI traces
It can be used as a baseline network model with no contention and no routing

## Slide 19: Configuring simple-net logp model
For mapping entities on ROSS MPI processes
Messages are broken into packets by the model-net layer
ROSS specific parameter (event size)
Startup delay in ns
Link bandwidth in MB/s (one link between each pair of nodes)
Configuration file can be found in codes/tests/conf/modelnet-test.conf

## Slide 20: Running a simple-net logp model
./tests/modelnet-test --sync=1 -- tests/conf/modelnet-test.conf
A simple test in which a simulated MPI rank sends message to the next rank, which replies back
Continues until a certain number of messages is reached

## Slide 21: DRAGonfly network model
Multiple forms of routing are supported: minimal, adaptive, non-minimal and progressive adaptive
Packet based simulation with credit based flow control
Uses multiple virtual channels for deadlock prevention
Dragonfly group
Dragonfly group
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
A Cray XC style dragonfly group
Dragonfly group as proposed by Kim, Dally et al.

## Slide 22: Configuring dragonfly network model
nw-lp is a simulated MPI process
A simulated dragonfly network node
A simulated dragonfly network router
For simulating multiple MPI processes per node  nw-lp=num-procs * number of network nodes
Self messages messages sent to the same network node
Overhead for sending self message can be configured
Configuration file can be found in codes/src/network-workloads/dragonfly-custom

## Slide 23: Configuring dragonfly network model
Router arrangement within a group. Should match the input network configuration
Buffer size of virtual channels can be configured
Number of compute nodes per router is configurable
Network configuration files – can be custom generated (see scripts/gen-cray-topo/README.txt).

## Slide 24: Running a dragonfly network simulation
Download the traces:
  wget https://portal.nersc.gov/project/CAL/doe-miniapps-mpi-traces/AMG/df_AMG_n1728_dumpi.tar.gz
Run the simulation:
  ./src/network-workloads/model-net-mpi-replay --sync=1 --disable_compute=1 --workload_type="dumpi" --workload_file=df_AMG_n1728_dumpi/dumpi-2014.03.03.14.55.50- --num_net_traces=1728 -- ../src/network-workloads/conf/dragonfly-custom/modelnet-test-dragonfly-edison.conf

## Slide 25: Fat tree network model
Full 3-level k=8 Fat-Tree with 128 compute nodes
Can simulate two and three level fat tree networks
Width of the tree (number of pods) can also be configured
Two forms of routing are supported:
  static: uses destination-based look-up tables
  adaptive: selects least congested output port
Packet based simulation with credit based flow control

## Slide 26: Fat Tree Network Configurations
Tapering can be used to connect more nodes to the leaf switches
  Reduces the bandwidth, switches and links at higher level
To get higher bandwidth, nodes can connect to multiple ports (multi-rail) in one or more plane (multi-plane)
  These configurations can also be tapered to reduce switches, links at higher levels
Model supports configurations for multiple rails, multiple plane and tapering

## Slide 27: Configuring fat tree network model
Nw-lp is a simulated MPI process
A simulated fat tree network node
Three simulated fat tree network switches (one in each level of the network)

## Slide 28: Configuring fat tree network model
Switch arrangement should match the input network configuration
Switch radix can be configured
Static routing requires precomputed destination routing tables
See:
https://github.com/codes-org/codes/wiki/codes-fattree#enabling-static-routing

## Slide 29: Slim fly network model
Fig. Slim Fly with q=5
Topology of interconnected router groups built with MMS graphs
The max network diameter is always 2
Packet based simulation with credit based flow control
Multiple forms of routing are supported:
  minimal: 2 virtual channels
  non-minimal: 4 virtual channels
  adaptive: 4 virtual channels
Notes: The two generator sets are the two sets of indices used to calculate connections between routers in the same subgraph.
The computation of generator sets is very non-trivial and it hasn’t been automated so far.
The two subgraphs span half the groups. The entire network of routers is logically broken into two subgraphs. Within each subgraph, routers are broken into groups.

## Slide 30: Configuring Slim Fly network model
Generator sets are set of indices used to calculate connections between routers in the same subgraph. They must be precomputed.
Router arrangement within a group.

## Slide 31: HYPER-X, Express mesh, and Torus
Express Mesh: low-diameter densely connected grids
  Allows for specifying connection gap
  Gap = 1 -> HyperX
Torus: based on a n-dimensional k-ary network topology
  Number of torus dimensions and length of each dimension can be configured
  Supports dimension order routing
Uses bubble escape virtual channel for deadlock prevention
Notes: - Used in Blue Gene and Cray XE and XT series of networks

## Slide 32: Arbitrary graphs
Can also input arbitrarily connected graphs
  Defined using DOT format
Static routing is required
  Generated using OpenSM, courtesy Jens Domke

## Slide 33
Interpreting simulation output

## Slide 34: Interpreting simulation output
Enabling lp-io-dir generates detailed network statistics files
Average and maximum times are reported for all the application runs
Network statistics (hops traversed, latency, routing etc.) are reported for the entire network
Detailed statistics for each MPI rank, network node, router, port are generated using lp-io-dir option
--lp-io-dir=my-dir can be used to enable statistics generation (Each lp writes it statistics to a summary file)
Application level statistics e.g. time spent in overall execution, communication, wait operations, amount of data transferred etc.

## Slide 35: Statistics reported by lp-io
Dragonfly-msg-stats:
  number of hops, packet latency, packets sent/received, link saturation time reported for each network node
Dragonfly-router-stats
  link saturation time each router port
Dragonfly-router-traffic
  Traffic sent for each router port
Fat tree and slim fly networks have similar statistics files.
Mpi-replay-stats (generated for any network model):
  bytes sent/received per MPI process
  time spent in communication per MPI process
  Number of sends and receives per MPI process

## Slide 36
Case study
Fit Fly: Interconnect Innovation through parallel simulation

## Slide 37
CODES is designed to help find answers to the “What If…” type questions in HPC Interconnection research

## Slide 38: MultI-Plane Networks
Single Plane
Dual Plane
Hand in hand with multi-rail networks
  Additional links for packet injection
Additional independent planes of routers
  Often sharing terminals across planes

## Slide 39: Slim Fly Network Topology
Routers in network are organized into groups
Each Router
  Some degree of Local connectivity
  Some degree of Global connectivity
  Some degree of Terminal connectivity
Guaranteed Diameter-2
Groups are divided into two subgraphs
  No global connections between two groups within same subgraph
Connections are determined via non-trivial generation method
  Makes it challenging to physically build

## Slide 40: Fit Fly
Multi-Planar Slim Fly Network
Planes share single set of terminals
Each plane follows same Slim Fly network generation method
Terminal to Router mapping is alternating mirrored on each new plane
  Increase path diversity
Slim Fly
Fit Fly

## Slide 41: More Rails = More Throughput
Fit Fly Based on previously validated Slim Fly Model
Additional planes bring additional throughput
Observed expected increase in throughput with synthetic uniform random traffic

## Slide 42: Experiments overview
Experiment Set 1
Cross Network
Experiment Set 2
Equalized Bandwidth

## Slide 43: Network Comparison: AMG 1728
Lower is better

## Slide 44: Network Comparison: MG 1000
Lower is better

## Slide 45: Discussion: Network Comparison
Slim Fly performed well against state of the art Dragonfly and Megafly networks
  Possible future exascale networks
Fit Fly showed great resilience to high levels of interference traffic
  Beat Slim Fly by an order of magnitude
Slim Fly and Fit Fly networks show great promise
  Low-diameter-high-path-diversity

## Slide 46: Equalized Bandwidth 12.5GiB/s – AMG 1728
Lower is better

## Slide 47: Equalized Bandwidth 25GiB/s – AMG 1728
Lower is better

## Slide 48: Discussion: Equalized Bandwidth
Equalizing the aggregate bandwidth across networks slightly reduced the advantage that Fit Fly had
  Fit Fly still pulled ahead
    Greater interference resilience
Additional planes of routers give less chance for any two packets to interact
  Less interference
  Less buffer wait time
  Increased Application Performance
More planes of cheaper routers may be a better option to single-plane-high-bandwidth networks

## Slide 49: Case Study: Conclusion
Fit Fly well outperforms state-of-the-art interconnects
More routers and planes = Less Interference
More routers = More Cost
  But cheaper routers and links could be used
CODES provides a strong environment for answering “What If…” questions and fostering future innovation in the field of HPC interconnection networks

## Slide 50: Running interconnect simulations
Checkout the exercises at the wiki link:
https://github.com/codes-org/codes/wiki/quick-start-interconnects

## Slide 51
Session II: Application simulation, workloads, MPI

## Slide 52: Four steps TO SIMULATIONS
Prototype system design
  Discussed in the previous session
  Set up using network parameters
Workload selection
  Depends on the use case
  Application traces
  Synthetic patterns
  Skeletons
Workload creation
Execution

## Slide 53
HPC Application Traces
MPI replay
Network Simulation
Simulation Suite
Network Model statistics
General framework for replaying traces on HPC interconnect simulation
CODES specific framework for replaying traces on HPC interconnect simulations
Notes: TODO: Animate the figure parts

## Slide 54: workloads
Synthetic Workloads:
  Follow specific communication pattern and a constant injection rate
  Often used to stress the network topology to identify best and worst case performance
  Examples include uniform random, all to all, bisection pairing, bit permutation
  Don’t require simulation of MPI operations
HPC Application Traces:
  Useful for network performance prediction of production HPC applications
  Trace size can be large for long running or communication intensive applications
  Potential to capture computation-communication interplay
  Require accurate simulation of MPI operations
  Simulation results can be complex to analyze
Intel SWM Online Workloads:
  Accurate workload representations
  Decoupled from original application
  Portable to arbitrary simulation environments
  Generates traffic on-the-fly
Notes: - TODO cite WSC paper here

## Slide 55: DUMPI mpi trace library
Provides trace collection and replay tools for MPI based applications
Trace collection is simple – link the MPI application with libdumpi
Trace can be replayed using libundumpi utility
Libundumpi provides callbacks you can use when MPI operations are replayed
Preserves the causality order of MPI operations
Captures detailed statistics for each MPI operation call

## Slide 56: Capturing application traces with dumpi
Repository can be cloned at:
  git clone https://github.com/sstsimulator/sst-dumpi.git
Configure and build using any MPI compiler
Make sure to use ‘—enable-libdumpi’ when configuring
Once installed, simply add ‘-L$(DUMPI_INSTALL) -ldumpi’ in your application
DUMPI traces will be generated automatically with each application run
Naming convention: dumpi-yyyy.dd.mm.hh.mm.ss-MPI-RANK-ID.bin
More information can be found at: https://github.com/sstsimulator/sst-dumpi
HPC application traces in DUMPI format: https://portal.nersc.gov/project/CAL/designforward.htm

## Slide 57: Generating OTF2 traces (1/2)
New Open Trace Format version 2 is supported by several tools
ScoreP - Scalable Performance Measurement Infrastructure for Parallel Codes
Tool suite with several libraries and helper tools
  http://www.vi-hps.org/projects/score-p/
Inside ScoreP source directory
  CC=mpicc CFLAGS="-O2" CXX=mpicxx CXXFLAGS="-O2" FC=mpif90 F77=mpif77 ./configure --without-gui --prefix=<SCOREP_INSTALL>
  make && make install
  Make sure ScoreP installation’s bin directory is in PATH
Simple case: change the application linker to LD = scorep --user --nocompiler --noopenmp --nopomp --nocuda --noopenacc --noopencl --nomemory <your_linker>

## Slide 58: Generating OTF2 traces (2/2)
Before running, set the following environment variables: export SCOREP_ENABLE_TRACING=1 export SCOREP_ENABLE_PROFILING=0 export SCOREP_MPI_ENABLE_GROUPS=ENV,P2P,COLL,XNONBLOCK
Turning tracing on/off: make sure these calls are synchronized
  #include <scorep/SCOREP_User.h>
  SCOREP_RECORDING_ON(); - start recoding
  SCOREP_RECORDING_OFF(); - stop recording
During compilation, add flags: -I$SCOREP_INSTALL/include -I$SCOREP_INSTALL/include/scorep -DSCOREP_USER_ENABLE
Trace target options export SCOREP_TOTAL_MEMORY=256M export SCOREP_EXPERIMENT_DIRECTORY=/p/lscratchd/<username>/...

## Slide 59: Tracing output
scorep-* directory generated with following content: scorep.cfg traces traces.def traces.otf2
scorep.cfg is human readable; can be used to verify if the environment is correctly generated
traces.otf2 is a binary meta-file
traces is a directory that contains the details
Use otf2-print utility in ScoreP bin to view the traces: otf2-print –L 0 traces.otf2

## Slide 60: Information captured in a typical trace (e.g. in DUMPI, OTF2)
Time stamp, t (rounded off) | Operation type | Operation data (only critical information is highlighted)
t = 10 | MPI_Bcast | root, size of bcast, communicator
t = 10.5 | MPI_Irecv | source, tag, communicator, req ID
t = 10.51 | user_computation | optional region name - “boundary updates”
t = 12.51 | MPI_Isend | dest, tag, communicator, req ID
t = 12.53 | user_computation | optional region name - “core updates”
t = 22.53 | MPI_Waitall | req IDs
t = 25 | MPI_Barrier | communicator

## Slide 61: Example to show the effect of replaying traces
Original Time stamps | Original duration | New Time stamps | New duration | Operation type
10 | 0.5 | 10 | 0.2 | MPI_Bcast
10.5 | 0.01 | 10.2 | 0.01 | MPI_Irecv
10.51 | 2 | 10.21 | 2 | user_computation
12.51 | 0.02 | 12.21 | 0.02 | MPI_Isend
12.53 | 10 | 12.23 | 10 | user_computation
22.53 | 2.47 | 22.23 | 0.03 | MPI_Waitall
25 | 1 | 22.26 | 1.7 | MPI_Barrier
Notes: TODO Nikhil: Explain in caption what the red color coding means.

## Slide 62: DUMPI vs OTF2
Most of the information in the trace format is the same
Different w.r.t. capturing of dynamically determined events: e.g. MPI_Waitany
DUMPI: stores all the information passed to the MPI call
  Simulation decides which request to fulfill: accurate resolution for target systems
  If the control flow of the program can change significantly due to the ordering of operations, simulations are not entirely correct
OTF2: stores only the information that is used (e.g. which request was satisfied)
  Accurately mimics the control flow of the trace run
  But does not accurately represent execution for the target system
Artifact of leveraging existing tools not originally intended for PDES!
Notes: A different system could capture both and allow PDES to decide which/hoe to use.

## Slide 63: Intel SWM Workloads
Open Source version hosted at https://github.com/codes-org/SWM-workloads
Built separately: a CODES-SWM interface has been developed
Includes several workloads including LAMMPS, Nekbone, Nearest Neighbor, HACC, MILC, Incast, Point-to-Point
Each workload is configured by its own JSON configuration file
  Specifies size
More CODES use information:
  https://github.com/codes-org/codes/wiki/online-workloads

## Slide 64
Simulating mpi

## Slide 65: MPI Simulation
Matching semantics and standard has to be followed for a correct simulation
  So obviously done
Eager – Rendezvous protocol
  Cutoff can be specified in the config
Library call overheads handled using a constant cost
Collectives:
  OTF2 based simulations implements them internally
  DUMPI based simulations use Cortex

## Slide 66: Translating mpi calls using cortex
Internally most MPI implementations support collectives by translating into point to point
Cortex comes with a set of translation functions to convert collectives into point to point using MPICH algorithms
When linked with DUMPI and CODES, Cortex translates MPI collectives into point to point sends/receives (simulated by CODES)
Cortex can also be used to implement your own translation functions (e.g. collective algorithms)
Cortex tutorial is available at : https://xgitlab.cels.anl.gov/mdorier/dumpi-cortex/wikis/home

## Slide 67: codes, cortex and dumpi interaction
DUMPI Application Trace
Cortex
MPI Collective calls
MPI send/recv/waits
CODES
MPI Simulation Layer
Model-net layer
Network Models
Translated sends/recvs

## Slide 68: mpi translation with cortex
To enable collective translation, install Cortex and reconfigure CODES with Cortex
Cortex available for download: git clone https://xgitlab.cels.anl.gov/mdorier/dumpi-cortex.git
cmake .. -G "Unix Makefiles" -DMPICH_FORWARD:BOOL=TRUE -DCMAKE_INSTALL_PREFIX=$HOME/CODES/install/cortex -DDUMPI_ROOT=$HOME/CODES/install/dumpi
See instructions at: https://xgitlab.cels.anl.gov/codes/codes/wikis/codes-cortex-install
Use –with-cortex=/path/to/cortex/install option
Notes: Uses a similar API as DUMPI but you don’t need to specify callbacks for all the MPI functions
In CODES, there are similar callback functions that simulate MPI operations like send, receive, wait
For collective operations, CODES calls Cortex callbacks that translate collectives into point to point

## Slide 69: In a nutshell: Replaying a single application trace
./bin/model-net-mpi-replay --sync=1 --disable_compute=1 --workload_type="dumpi" --workload_file=dumpi-2014.03.03.14.55.50- --num_net_traces=1728 -- modelnet-test-dragonfly-edison.conf
Runtime options
  --workload_type: “dumpi” or “online” for SWM
  --num_net_traces : Number of input network traces
  --workload_file: DUMPI trace file
  Network configuration file: Any of the network files (number of simulated ranks > number of ranks in trace)
  --lp-io-dir (optional): Generates detailed network counters and statistics
  --lp-io-use-suffix (optional): Generates a unique directory per run
  --disable_compute (optional): disable any compute time between MPI events
  --workload_conf_file: for SWM, specifies name of workload to be used
For running parallel simulations, use mpirun and –sync=3
Notes: MOVE it after setup

## Slide 70
Simulating multiple jobs on the network

## Slide 71: Replaying multiple jobs
./src/network-workloads/model-net-mpi-replay --sync=1 --disable_compute=1 --workload_type="dumpi" --workload_conf_file=multiple-workloads.conf –alloc_fil -- modelnet-mpi-test-dragonfly.conf
For multiple jobs, two of the arguments are different:
  Workload_file: Has information on the dumpi/SWM traces for each application
  Alloc_file: List of simulated MPI ranks to be assigned to each job

## Slide 72: Example workload file
Left column: Number of application ranks per job
Right column: Path and prefix of DUMPI traces for each job – or name of SWM
  Combination SWM and Dumpi slated for future
  Currently can only combine DUMPI+DUMPI/Synthetic and SWM+SWM/Synthetic

## Slide 73: Example job allocation file
List of MPI ranks for each job
There is a job entry per line
Example at the top shows job placement being done in a linear scheme
Example below shows job placement in a random fashion (assumes one rank per node).

## Slide 74: Generating job allocations using different schemes
Multiple schemes to map jobs onto the network
  Randomly selected nodes
  Contiguous or linear
  Randomly selected switches (ranks ordered on nodes attached to a switch)
  Clustered placement
  …
Scripts can be used to generate job allocation files with any of the above schemes
CODES keeps track of the job ID and provides it in simulation output
Some python scripts can be found in scripts/allocation_gen

## Slide 75
Session iii: storage models and synthetic traffic generation

## Slide 76: Goals of the session
How to do storage placement on networks?
How to generate background network traffic?
Using model-net API
PDES and Networks Internal
Continue with hands on exercises

## Slide 77
Storage placement on interconnects

## Slide 78: Storage placement on hpc systems
* Image credit: On the role of burst buffers in Leadership class storage system by N. Liu et al. in MSST 2012
Example burst buffer placement on a Blue Gene system
Example burst buffer placement on a dragonfly system

## Slide 79: Modeling burst buffer with codes
General purpose model for read and write operations
Concurrent, pipelined RDMA requests
Comprises of the following:
  a storage manager
  a disk/local storage model
  A resource tracker
Placement of storage over the network can be modified using the network config file

## Slide 80: Protocol for write operations

## Slide 81: Using the storage model
codes_store_init_req (is_write, priority, obj_id, xfer_offset, xfer_size, codes_req)  For initializing the request
codes_store_send_req(codes_req, dest_id, sender, network_id, mapping_context, ..)  For sending the request
codes_store_send_req_rc  For reverse computation
Repo available at:https://xgitlab.cels.anl.gov/codes/codes-storage-server

## Slide 82: Configuring storage over the network
Number of concurrent requests
Buffer size for each thread
Size of the Memory (RAM)
Storage size (for disk/LSM)
Aggregate memory+storage size
Disk bandwidth/seek configuration

## Slide 83: Configuring storage over the network
Two storage manager entities per 60 clients/compute nodes (Cray Cori configuration)
Local storage model entity (disk). One to one correspondence
A total of 64 network nodes
If the data from burst buffer needs to be drained to the external storage entity
Dummy nodes are to balance
node to router ratio for BB routers

## Slide 84
Generating background network traffic

## Slide 85: Why background traffic?
On production HPC systems, a significant fraction of network nodes can be occupied
How to introduce communication interference if a single application trace is being replayed on the simulation?
Running multiple traces at a large-scale can be expensive
One solution is to mix synthetic traffic patterns and HPC application traces

## Slide 86: Example Synthetic patterns
Uniform Random: A network node is equally likely to send to any other network node (traffic distributed throughout the network)
All to All: Each network node communicates with all other network nodes
Nearest neighbor: A network node communicates with near by network nodes (or the ones that are at minimal number of hops)
Permutation traffic: Source node sends all traffic to a single destination based on a permutation matrix
Bisection pairing: Node 0 communicates with Node ‘n’, node 1 with ‘n-1’ and so on.
…

## Slide 87: Synthetic traffic in codes
Typical patterns supported are uniform random and nearest neighbor.
All to all and stencil patterns have been tested (pending integration)
See src/network-workloads/model-net-synthetic-custom-dfly.c and related files
* Code snippet from synthetic workload generator

## Slide 88: Generating background traffic with codes
Communication based on uniform random traffic
Kicks off when the main workload starts
A notification is sent to the background traffic node to stop generating traffic once the main workload finishes
How to enable synthetic traffic generation?
Simply add “synthetic” instead of DUMPI trace path in workloads config file

## Slide 89
PDES and network internals

## Slide 90: Discrete Event Simulation (DES)
Computer model for a system where changes in the state of the system occur at discrete points in simulation time
In this model, each component of the system being simulated is represented independently via their
State variables
Virtual time
Events - scheduled on it and by it

## Slide 91: DES example: air traffic
Example from slides by Prof Carothers, RPI
Event scheduling from one component to another progresses and
coordinates virtual time across components
each plane is independently represented
as a component, so is the runway

## Slide 92: Implementing DES
ROSS lets users define LP (logical processes) on which events can be scheduled with time stamps
Each LP can have a local state that is accessible and modified only when events are executed on it

## Slide 93: ROSS LP
tw_lptype model_lps[] = {
{
(init_f) model_init,
(event_f) model_event,
(revent_f) model_event_reverse,
(final_f) model_final,
(map_f) model_map,
sizeof(state)
},
};

## Slide 94: Example of an event function
Typical events act based on “type” and “content” of the message

## Slide 96: ROSS’s law of optimistic execution: for every forward action, you must tell ROSS how to go backwards

## Slide 98: Application simulation IN CODES
PE 0 (mpi rank or end points)
— computation tasks, communication logs, or algorithmic state
— expected messages
— pending messages
— progress overheads
Routers
— routing tables
— data on buffers connecting to other routers and NIC
— congestion control scheme
— pending packets in each buffer
— link bandwidth
— router delays
NIC
— messages to be transmitted
— packetization status of messages being transmitted
— data on buffers connecting to router
— NIC delay
— bandwidth to routers
message send
message arrive
task complete
packet send
ack/token send
packet arrive
ack/token send
packet send
ack/token send
packet arrive
ack/token arrive

## Slide 99: Available models, features, and adding a new network models
Available: simple-net model, torus, dragonfly-(custom), fat-tree, slim fly, express-mesh/hyperX
Typical model consist of NIC (terminals) and switches/routers
NICs
  Common code available for within-node, message ordering, etc
  Plugin code for individual network
Switch/routers
  Entirely within a network model
But, a significant fraction of node is similar for NIC plugin and switch!

## Slide 100: NIC Common
Types of queues:
fifo
round-robin
priority
Other params
intra_bandwidth (10)
node_copy_queues (4)

## Slide 101: NIC Network Specific
struct model_net_method torus_method =
{
.mn_configure = torus_configure,
.mn_register = NULL,
.model_net_method_packet_event = torus_packet_event,
.model_net_method_packet_event_rc = torus_packet_event_rc,
.model_net_method_recv_msg_event = NULL,
.model_net_method_recv_msg_event_rc = NULL,
.mn_get_lp_type = torus_get_lp_type,
.mn_get_msg_sz = torus_get_msg_sz,
.mn_report_stats = torus_report_stats,
.mn_collective_call = NULL,
.mn_collective_call_rc = NULL,
.mn_sample_fn = NULL,
.mn_sample_rc_fn = NULL,
.mn_sample_init_fn = NULL,
.mn_sample_fini_fn = NULL
};

## Slide 102: NIC Network Specific

## Slide 103
CONTRIBUTING:
Fork off on the github repository
Add new features
Submit a pull request!
Thank-you

## Slide 104
ADDITIONAL MATERIAL

## Slide 105
Codes installation

## Slide 106: installation & setup 1/2
ROSS INSTALLATION
  Download ROSS repo: git clone https://github.com/ROSS-org/ROSS
  Configure by making a build directory: cd build
  ARCH=x86_64 CC=mpicc CXX=mpicxx cmake
  -DCMAKE_INSTALL_PREFIX=../install ../
  make –j 3 && make install
CODES INSTALLATION
  Download CODES repo: git clone https://github.com/codes-org/codes
  ./prepare.sh
  Configure in build directory: cd build
../configure --prefix=/path/to/install CC=mpicc CXX=mpicxx PKG_CONFIG_PATH=/path/to/ross/install/lib/pkgconfig
  Do both make && make tests

## Slide 107: Installation & setup 2/2
DUMPI INSTALLATION
  git clone https://github.com/sstsimulator/sst-dumpi
  CFLAGS="-DMPICH_SUPPRESS_PROTOTYPES=1 -DHAVE_PRAGMA_HP_SEC_DEF=1"
  ./bootstrap.sh
  ./configure --enable-libundumpi CC=mpicc --prefix=$INSTALL_PATH
  Use –with-dumpi=/path/to/dumpi/install option to enable DUMPI with CODES
OTF2 and BigSim based Tracing
  ScoreP/OTF2: http://www.vi-hps.org/projects/score-p/
  Charm++/BigSim:http://charm.cs.illinois.edu/manuals/html/bigsim/manual.html
  TraceR: https://github.com/LLNL/tracer/
For installation details and documentation see:
  https://xgitlab.cels.anl.gov/codes/codes/wikis/home
  https://xgitlab.cels.anl.gov/codes/codes/wikis/installation

## Slide 108
MORE ON TraceR

## Slide 109: TraceR – a layer for configurable replay of application traces
Capture application behavior by tracing runs on existing systems
Simulation of traffic flow on NICs and networks
Reproducing the execution: applications’ behavior,
job placement and mapping, job scheduling, MPI/Charm++, etc.

## Slide 110: DOCUMENTATION
Distributed with TraceR source code
README.md – getting started
README.OTF - OTF2 installation and usage
docs/UserWriteUp.txt – detailed workflow and usage
utils/README – job placement and task mapping

## Slide 111: Installing TraceR (1/4)
Hosted on github: https://github.com/LLNL/tracer/
git clone and follow README.md
Download and install ROSS
  Last verified commit provided
Download and install CODES
  Last verified commit provided

## Slide 112: Installing TraceR (2/4)
Choose a trace format: BigSim or OTF2
For BigSim, download Charm++
  git clone http://charm.cs.uiuc.edu/gerrit/charm
Assuming MPI is available, install two flavors of Charm++
  For compiling codes for trace generation ./build bgampi mpi-linux-x86_64 bigemulator –O2
  For compiling TraceR ./build charm++ mpi-linux-x86_64 bigemulator --with-production

## Slide 113: Installing TraceR (3/4)
For OTF2, download ScoreP
  http://www.vi-hps.org/projects/score-p/
Inside ScoreP source directory
  CC=mpicc CFLAGS="-O2" CXX=mpicxx CXXFLAGS="-O2" FC=mpif90 F77=mpif77 ./configure --without-gui --prefix=<SCOREP_INSTALL>
  make && make install
  Make sure ScoreP installation’s bin directory is in PATH

## Slide 114: Installing TraceR (4/4)
In tracer/Makefile.common
Set ROSS to ROSS’s installation directory
Set CODES to CODES’s installation directory
If using BigSim,
  Set CHARMPATH
  SELECT_TRACE = -DTRACER_BIGSIM_TRACES=1
If using OTF2,
  Make sure ScoreP installation’s bin directory is in PATH
  SELECT_TRACE = -DTRACER_OTF_TRACES=1
make: generates traceR executable

## Slide 115: More on Generating OTF2 traces
ScoreP macros can be used to mark special regions
  SCOREP_USER_REGION_BY_NAME_BEGIN( regionname, SCOREP_USER_REGION_TYPE_COMMON)
  SCOREP_USER_REGION_BY_NAME_END(regionname)
Printing simulation time at locations of interest:
Region name with prefix TRACER_WallTime_<any_name> prints current time during simulation with tag <any_name>.

## Slide 116: More on Generating OTF2 traces
Simulation time looping:
Region name TRACER_Loop can be used to mark beginning and ending of a code loop (currently once)
In future, region names will be used for
  Targeted kernel time modifications
  Targeted message size modifications

## Slide 117: Code example for tracing with OTF2
int main(int argc, char **argv) {
MPI_Init(&argc, &argv);
SCOREP_RECORDING_OFF();
//initializaton code
MPI_Barrier(MPI_COMM_WORLD);
SCOREP_RECORDING_ON();
SCOREP_USER_REGION_BY_NAME_BEGIN ("TRACER_Loop", SCOREP_USER_REGION_TYPE_COMMON);
if(!myRank)
SCOREP_USER_REGION_BY_NAME_BEGIN ("TRACER_WallTime_Total", SCOREP_USER_REGION_TYPE_COMMON);
startTime = MPI_Wtime();
while(iterations < MAX_ITER) {
if(myRank == 0)
SCOREP_USER_REGION_BY_NAME_BEGIN ("TRACER_WallTime_InLoop", SCOREP_USER_REGION_TYPE_COMMON);
//kernel and other code
}
SCOREP_USER_REGION_BY_NAME_END ("TRACER_Loop");
MPI_Barrier(MPI_COMM_WORLD);
endTime = MPI_Wtime();
if(!myRank)
SCOREP_USER_REGION_BY_NAME_END ("TRACER_WallTime_Total");
SCOREP_RECORDING_OFF();

## Slide 118: Running TraceR
A typical run command: mpirun -np 8 ./traceR --sync=3 --nkp=16 --extramem=100000 --max-opt-lookahead=1000000 --timer-frequency=1000 –lp-io-dir=stats-dir -- torus.conf tracer_config
In green, ROSS options
  --nkp : how many KPs to create per PE = total LPs/<-np>
  --extramem : how many ROSS messages to allocate = 100K should work for most cases
  --max-opt-lookahead : optimistic leash = 1 millisecond is a good number

## Slide 119: Running TraceR
A typical run command: mpirun -np 8 ./traceR --sync=3 --nkp=16 --extramem=100000 --max-opt-lookahead=1000000 --timer-frequency=1000 –lp-io-dir=stats-dir -- torus.conf tracer_config
TraceR-CODES options
  --timer-frequency : how frequently to print progress of task completion; optional, default = 5000
  --lp-io-dir : where to write output stats; optional; code fails if the directory exists to avoid over-writing
  torus.conf : network config file
  tracer_config : TraceR config file

## Slide 120: TraceR parameter in network file
server in MODELNET_GRP
  Number of processes associated with a switch
  Assigned in a round-robin manner to nodes
soft_delay in PARAMS
  Approximate overhead of making an MPI/runtime call
  In nanoseconds
rdma_delay in PARAMS
  Overhead of using RDMA call in rzv protocol, in nanoseconds
eager_limit in PARAMS
  Switch over point between eager and rzv protocols, in bytes
copy_per_byte in PARAMS
  Copy cost for a byte, in nanoseconds per byte

## Slide 121: TraceR config file (1/2)
Format:
<global map file> or NA
#jobs
<path to job traces> <task mapping file or NA> <#ranks> <loop iterations>
Example:
global_map.bin
2
traces-64/traces.otf2 job0 64 1
traces-32/traces.otf2 job1 32 1

## Slide 122: TraceR config file (2/2)
At the end of file,
E <job id> scale_all <scale factor>
  Inverse scales computation time by the given factor
  E.g. : E 0 scale_all 40
S <job id> <msg size> <replace by>
  Change the size of message
  Under review, to be merged

## Slide 123: Sample output
PE0 - LP_GID:0 : START SIMULATION, TASKS COUNT: 245611, FIRST TASK: 0, RUN TIME TILL NOW=70.000000 s, CURRENT SIM TIME 1.005877
[ 0 0 : time at task 0/245611 0.000000 ]
[ 0 0 : Begin TRACER_WallTime_MainLoop 0.000001 ]
[ 0 0 : time at task 100/245611 0.000663 ]
[ 0 0 : Begin TRACER_WallTime_NextTrajec 0.001175 ]
[ 0 0 : time at task 200/245611 0.003104 ]
….
….
[ 0 0 : time at task 245600/245611 1.485123 ]
[ 0 0 : End TRACER_WallTime_NextTrajec 1.485264 ]
[ 0 0 : End TRACER_WallTime_MainLoop 1.485265 ]

## Slide 124
Case studies with codes-tracer

## Slide 125
Quantify the effectiveness of multiple network rails in increasing network performance
Evaluate job placement methodologies and routing choices to maximize the throughput of a multi-rail fat-tree network
Investigate network performance gains offered by multiple rails in response to increased compute performance of high-density compute nodes
Improve routing, injection and job allocation design choices of multi-rail fat-tree networks to maximize individual application and system wide performance
Related papers
Jain et al. Predicting the Performance Impact of Different Fat-Tree Configurations (To appear in Supercomputing 2017)
Wolfe et al. Preliminary Performance Analysis of Multi-Rail Fat-tree Networks (CCGRID 2017)
Fat-tree strong scaling rail performance
Multi-application workload
Linear system improvement
Evaluating Methods for Effective Fat-tree Utilization
Notes: Simulation Configuration:
  3,564 node fat-tree using 36-port switches
  All configurations use EDR 12.5Gb/s speeds
  13,824 ranks AMG
  1,000 ranks CR
  10,648 ranks MG
Comments on Results:
  Some applications such as Multigrid with bursty periods of large data transfers can benefit from the additional bandwidth and diversity of additional rails
  Other applications like AMG and Crystal Router that have synchronized communication patterns of small data transfers do not observe performance improvements

## Slide 126: Visualizing HPC Interconnect Performance
K. Li, M. Mubarak, R. Ross et al. “Visual Analytics Techniques for Exploring the Design-space of large-scale high-radix networks”, to appear in IEEE Cluster 2017
Comparing job placement schemes using the CODES simulation framework of the high-radix dragonfly network running the Algebraic Multigrid Solver (AMG), AMR BoxLib and MiniFE applications. The visualizations show the aggregated network view of all the routers and network links.

## Slide 127: Accelerating Collective Communication on Dragonfly Networks
Need to design new scalable collective algorithms for high-radix interconnects
Investigate the parameter space of these algorithms, and the effects of cross-application communication interference
Designed/evaluated several collective algorithms for Dragonfly networks
M. Dorier et al. “Evaluation of Topology-Aware Broadcast Algorithms for Dragonfly Networks ”, IEEE Cluster 2016
(a) Tree (Non topology aware) (b) Local Links First (topology-aware) (c) Global Links First

## Slide 128
Using model-net api

## Slide 129: configuration
Model-net– An abstraction layer on top of network models – topology details are specified through the config files
A valid network configuration file – examples can be found in the repo
Network model must be registered – model_net_register
CODES mapping must be setup – codes_mapping_setup
Use model-net function calls – model_net_event(network id, source, destination, message size,…)
Example of using model-net – tests/model-net-test.c